## Slide 1: Chapter 11: Sequential Circuits and Finite State Machines
Notes: Welcome to sequential circuits and Finite State Machines.
This will be the last chapter to have homework assigned.
We are in the home stretch!

## Slide 2: Sequential Circuits
Combinational logic
  Need immediate application of Boolean function to a set of inputs
Will not work when circuit needs to change value with consideration to current state and inputs
  Need to “remember” the current state
Sequential logic circuits provide this functionality
Notes: Combinational logic circuits are perfect for situations when we require the immediate application of a Boolean function to a set of inputs.
There are other times, however, when we need a circuit to change its value with consideration to its current state as well as its inputs.
  These circuits have to “remember” their current state.
Sequential logic circuits provide this functionality for us.

## Slide 3
Sequential logic circuits require events to be sequenced
Clocks
  Control state changes
  Special circuit that sends electrical pulses through a circuit
  Produce electrical waveforms as shown below
Sequential Circuits
Notes: As the name implies, sequential logic circuits require a means by which events can be sequenced.
State changes are controlled by clocks.
  A “clock” is a special circuit that sends electrical pulses through a circuit.
Clocks produce electrical waveforms such as the one shown below.

## Slide 4
State changes occur in sequential circuits at clock ticks
Circuits can change state
  on the rising edge -or-
  falling edge -or-
  when the clock pulse reaches its highest voltage
Sequential Circuits
Notes: State changes occur in sequential circuits only when the clock ticks.
Circuits can change state on the rising edge, falling edge, or when the clock pulse reaches its highest voltage

## Slide 5
Edge-triggered circuits change state on
  the rising edge of the clock pulse
  or falling edge of the clock pulse
Level-triggered circuits change state when
  clock voltage reaches highest or lowest level
Sequential Circuits
Notes: Circuits that change state on the rising edge, or falling edge of the clock pulse are called edge-triggered.
Level-triggered circuits change state when the clock voltage reaches its highest or lowest level.

## Slide 6
Sequential circuits rely on feedback
Feedback
  output is looped back to the input
Example of this concept shown below
Sequential Circuits
  If Q is 0 it will always be 0, if it is 1, it will always be 1. Why?
Notes: To retain their state values, sequential circuits rely on feedback.
Feedback in digital circuits occurs when an output is looped back to the input.
A simple example of this concept is shown below.
  If Q is 0 it will always be 0, if it is 1, it will always be 1. Why?
If it is 0 here, it will be 1 here and it will be 0 here. This will be true at each clock tick. Remember we are including time now.
If it is 1 here, it will be 0 here and it will be 1 here.

## Slide 7
SR Latch (flip-flop)
  “SR” stands for set/reset
  most basic sequential logic components
SR latch circuit & block diagram shown below
Sequential Circuits
Notes: You can see how feedback works by examining the most basic sequential logic components, the SR Latch (flip-flop).
  The “SR” stands for set/reset.
The internals of an SR latch are shown below, along with its block diagram.
Note – the two screen shots here are what is expected for the discussion question this week.

## Slide 8
Behavior of SR latch
  described by a characteristic table
Q(t)
  value of the output at time t
Q(t+1)
  value of Q after the next clock pulse
Sequential Circuits
x | y | out = x NOR y
0 | 0 | 1
1 | 0 | 0
0 | 1 | 0
1 | 1 | 0
Notes: The behavior of an SR latch is described by a characteristic table.
Q(t) means the value of the output at time t.
Q(t+1) is the value of Q after the next clock pulse
<click>
Let’s add the truth table for NOR as a reference.
Here are the values at the initial state with S & R at zero.
If R – reset goes to 1, then Q is reset to 0 and Q-bar is reset to 1
If S – signal goes to1, then Q goes to 1 and Q bar goes to 0
Let’s draw the truth table for the SR Latch.

## Slide 9
SR latch- three inputs:
  S, R, current output: Q
Note: two undefined values
  S and R are both 1 –
  SR flip-flop is unstable
Sequential Circuits
Notes: The SR latch actually has three inputs: S, R, and its current output, Q.
Thus, we can construct a truth table for this circuit, as shown at the right.
Notice the two undefined values. When both S and R are 1, the SR flip-flop is unstable.

## Slide 10
If inputs to an SR latch will never both be 1
  Then circuit will never be unstable
Modified SR latch
  Provides stable state when both inputs are 1
Modified flip-flop is called JK flip-flop
“JK” is in honor of Jack Kilby
Sequential Circuits
Notes: If we can be sure that the inputs to an SR latch will never both be 1, we will never have an unstable circuit. This may not always be the case.
The SR latch can be modified to provide a stable state when both inputs are 1.
The Modified flip-flop is called a JK flip-flop, shown here.
The “JK” is in honor of Jack Kilby.

## Slide 11
JK flip-flop
  Modified SR flip-flop
  Adding 2 ANDs
Characteristic table indicates
  stable for all inputs
Sequential Circuits
Notes: At the right, we see how an SR flip-flop can be modified to create a JK flip-flop by adding two ANDs.
The characteristic table indicates that the flip-flop is stable for all inputs.

## Slide 12
D flip-flop – Data flip-flop
  Another modification of SR flip-flop
  Characteristic table is shown
Output changes
  when the value of D changes
  Stores D (data) until next clock pulse
Sequential Circuits
Notes: Another modification of the SR flip-flop is the D flip-flop, shown below with its characteristic table.
You will notice that the output of the flip-flop remains the same during subsequent clock ticks.
The output changes only when the value of D changes. This is used to store a data values until the D input changes.

## Slide 13
D flip-flop
  fundamental circuit of computer memory
Block diagram & Characteristic table for D flip-flop are shown below
Sequential Circuits
Notes: D flip-flop is the fundamental circuit of computer memory.
  D flip-flops are usually illustrated using the block diagram shown below.
And the characteristic table for the D flip-flop is shown at the right.

## Slide 14
T flip-flop – Toggle flip-flop
  Only one input T
Output changes
  If T=0 – state remains the same
  If T=1 – state toggles from 0 to 1 or from 1 to 0
Block diagram & Characteristic table for T flip-flop are shown below
Sequential Circuits
Notes: T flip-flop – Toggle flip-flop
  Only one input T
Output changes
  If T=0 – state remains the same
  If T=1 – state toggles from 0 to 1 or from 1 to 0
Block diagram & Characteristic table for T flip-flop are shown below

## Slide 15
Characteristic tables or finite state machines (FSMs)
  Express behavior of sequential circuits
  FSMs consist of
    set of nodes that hold the states of the machine
    set of arcs that connect the states
Moore and Mealy machines are two types of FSMs
  Moore machines place outputs on each node
  Mealy machines present their outputs on the transitions
  They are equivalent
Textbook uses Mealy Machine Convention
Sequential Circuits
Notes: The behavior of sequential circuits can be expressed using characteristic tables or finite state machines (FSMs).
  FSMs consist of a set of nodes that hold the states of the machine and a set of arcs that connect the states.
Moore and Mealy machines are two types of FSMs that are equivalent.
  They differ only in how they express the outputs of the machine.
Moore machines place outputs on each node, while Mealy machines present their outputs on the transitions.
Our textbook uses the Mealy Machine Convention

## Slide 16
Behavior of JK flop-flop is depicted below
Sequential Circuits
Moore machine
Mealy machine
Notes: The behavior of JK flop-flop is depicted below by a Moore machine on the left and a Mealy machine on the right.

## Slide 17
Behavior of Moore and Mealy machines is identical
Implementations differ
Implementation of Moore machine
Sequential Circuits
Notes: Although the behavior of Moore and Mealy machines is identical, their implementations differ.
Here is the implementation of the Moore machine

## Slide 18
Implementation of Mealy machine
Sequential Circuits
Notes: And here is the implementation of the Mealy machine

## Slide 19
Sequential circuits are used for “stateful” applications
Stateful application - next state of the machine
  Depends on the current state of the machine
  Depends on the input.
Stateful application requires
  Combinational and
  Sequential logic
Sequential Circuits
Notes: Sequential circuits are used anytime that we have a “stateful” application.
  A stateful application is one where the next state of the machine depends on the current state of the machine and the input.
A stateful application requires both combinational and sequential logic.
The following slides provide several examples of circuits that fall into this category.

## Slide 20
4-bit register consisting of D flip-flops on the right
Usual block diagram below
Sequential Circuits
Notes: This illustration shows a 4-bit register consisting of D flip-flops. You will usually see its block diagram as it is below instead.

## Slide 21
Sequential Circuits
Notes: Here is a larger memory configuration with D Flip-Flops.

## Slide 22
Binary counter
Low-order bit is complemented at each clock pulse
Whenever it changes from 0 to 1, the next bit is complemented, and so on through the other flip-flops.
Sequential Circuits
Notes: A binary counter is another example of a sequential circuit.
The low-order bit is complemented at each clock pulse.
Whenever it changes from 0 to 1, the next bit is complemented, and so on through the other flip-flops.

## Slide 23: Finite State Machines
Finite State Machine - tool to model sequential logic components
  Mealy/Moore machines describe sequential logic
  Finite State Machines are used to design control units for CPUs
Finite state machine consists of
  a finite number of states represented by the different values stored in a register
  a number of external inputs and external outputs
  boolean functions for the outputs of the machine according to the current state
  boolean functions to determine the next state according to current state and the current values of the external inputs
Notes: The Finite State Machine is tool to model sequential logic components in computer organization.
  We saw these Mealy/Moore machines in describing sequential logic.
  finite state machines are primarily used in the design of control units for CPUs.
A finite state machine consists of
  a finite number of states represented by the different values stored in a register
  a number of external inputs and external outputs
  boolean functions for the outputs of the machine according to the current state
  boolean functions to determine the next state according to current state and the current values of the external inputs

## Slide 24: Finite State Machines
Design of a sequential circuit
  More difficult because of "statefullness" of the circuit components.
    First develop a finite state machine (FSM)
      Consists of states and inputs
    State and inputs determine next state and possible outputs
    From FSM model, produce state table
    From state table, produce sequential circuit
Notes: We want to design a sequential circuit.
  More difficult because of "statefullness" of the circuit components.
    First develop a finite state machine (FSM)
    It consists of states and inputs.
    The State and inputs determine next state and possible outputs.
    From the model, a state table can be produced – like the truth tables for combinational circuits.
    From state table, the sequential circuit can be produced.

## Slide 25
Finite State Machine is represented by:
  state transition diagram
    each node represents a state
    the edge from state s1 to s2 with label for the external input value represents that state transition from s1 to s2 under the condition of the inputs described by the label
Finite State Machines
Notes: Finite State Machine can be represented by a state transition diagram where
    each node represents a state
    and the edge from state s1 to s2 with label for the external input value represents that state transition from s1 to s2 under the condition of the inputs described by the label.

## Slide 26
  state of truth tables to describe the state transition functions where
    the inputs of the tables are the binary values of the current state and the current external inputs
    the outputs of the functions are the binary values of the next state of the transition
Finite State Machines
Notes:   It can also be represneted by a state of truth tables to describe the state transition functions where
    the inputs of the tables are the binary values of the current state and the current external inputs
    the outputs of the functions are the binary values of the next state of the transition.

## Slide 27
Example: 3-bit up counter - finite state machine with
  8 states represented by a 3-bit register (3 D flip-flops) named as Q2, Q1, Q0
  no external inputs
  the following state transition diagram
000
001
010
011
100
101
110
111
Finite State Machines
Notes: For example, a 3-bit up counter is a finite state machine which
  has 8 states represented by a 3-bit register (3 D flip-flops) named as Q2, Q1, Q0
  has no external inputs
  has the following state transition diagram

## Slide 28
Implementation of finite state machine
  state transitions - implemented by the combinational logic for the boolean functions which input:
    the current state and
    the current value of external inputs
  use the outputs for the D inputs of the D flip-flops
  So next state is reached at beginning of next clock tick
Finite State Machines
Notes: Implementation of finite state machine
  the state transitions are implemented by the combinational logic for the boolean functions which take
    the current state and
    the current value of external inputs
  as inputs and use the outputs for the D inputs
  of the D flip-flops so that the next state can be reached at the beginning of the next clock tick on the rising edge.

## Slide 29: Mealy FSM
Output Is a Function of a Present State and Inputs
Memory
(register)
Transition
function
Output
function
Inputs
Present State
Next State
Outputs
Notes: Here is the implementation of the Mealy machine again with color codes with a bit different labels to relate it to the next slide.

## Slide 30: Mealy Machine
Describe Outputs as Concurrent Statements Depending on State and Inputs
state 1
state 2
transition condition 1 /
output 1
transition condition 2 /
output 2
Notes: Here is the basic definition of the Mealy machine and we will apply it to the J-K flip-flop.
Let’s start at State A. It is when the output is 0.
If 00 or 01 are input at the next tick, then the self arc indicates that the output will be zero and the state will remain at A.
If while at State A, inputs of 10 or 11 occur at the next tick, then this arc indicates that the output will change to 1 and the state will change to B.
While at State B, if 10 or 00 are input at the next tick, then the self are indicates that the output will be one and the state will remain at B.
If while at State B, inputs of 01 or 11 occur at the next tick, then this arc indicates that the output will change to 0 and the state will change to A.

## Slide 31: JK Flip-flop Example
Recall when J=1, sets flip-flop to 1
when K=1, sets flip-flop to 0
State table shown below
Notes: Recall when J=1, sets flip-flop to 1
when K=1, sets flip-flop to 0
The state tables are shown here. The one on the left shows all rows and the one on the right is simplified with don’t cares.
Note that each of the lines on the table on the right represents one arc in the finite state machine shown in the previous slide.

## Slide 32: Finite State Machines
Example 1: Alarm clock FSM example
  start with a state table
  then create state "machine“
    represent states as circles
    each transition (action) is represented as an arc
  FSM arcs must be mutually exclusive: cannot have two arcs with same input conditions (aka non-deterministic FSM).
Notes: Let’s look at an Alarm clock FSM example
  start with a state table, then create state "machine“
  represent states as circles
  each transition (action) is represented as an arc
  FSM arcs must be mutually exclusive: cannot have two arcs with same input conditions (aka non-deterministic FSM).

## Slide 33: FSM Alarm Clock Example
Events:
  Wake up at fixed time every day
  Weekends: you don’t need alarm, so you wake up, turn off the alarm and resume sleep
FSM modeling this chain of events, with:
  Three states:
    Asleep
    Awake but still in bed
    Awake and up
  Inputs:
    Alarm
    Weekday (determines you how to react to alarm)
  Outputs:
    Turn off the alarm
Notes: The Events for this are:
  Wake up at fixed time every day
  Weekends: you don’t need alarm, so you wake up, turn off the alarm and resume sleep
FSM modeling this chain of events, with:
  There are three states:
    Asleep
    Awake but still in bed
    Awake and up
  There are two Inputs:
    Alarm
    Weekday (determines you how to react to alarm)
  There is one Output:
    Turn off the alarm

## Slide 34: State tables
Similar to the truth table
Doesn’t contain the system clock when specifying its transitions
All the transitions occur on positive edge of the clock unless otherwise stated
Present State | Inputs | Next State | Outputs
Notes: State tables are similar to truth tables.
It doesn’t contain the system clock when specifying its transitions (it is implicit that transitions occur only when allowed by clock)
Unless different stated, all the transitions are occurring on the positive edge of the clock

## Slide 35: Alarm clock state table
Asleep and alarm rings
  Transition from being asleep to being awake in bed
  Turn off the alarm
Awake in bed and Weekday
  You get up
Awake in bed and not Weekday
  You go back to sleep
Table doesn’t cover what you wouldn’t do…
  (i.e. Asleep and the alarm is off, you remain asleep, etc..)
Present State | Alarm | Weekday | Next State | Turn off alarm
Asleep | On | X | Awake in bed | Yes
Awake in bed | Off | Yes | Awake and up | No
Awake in bed | Off | No | Asleep | No
Notes: When you are asleep and alarm rings, you go from being asleep to being awaked in bed; you also turn off the alarm
  If you are awake in bed and it is a weekday, You get up
  If you are awake in bed and it is not a weekday, You go back to sleep
This table doesn’t cover what you wouldn’t do…(i.e. if you are asleep and the alarm doesn't go off, you remain asleep, etc..)

## Slide 36: Alarm clock state table
Covers all the cases
  First row: Asleep and the alarm is off so you remain asleep
  Last row : Awake and up so you remain awake and up
  Third row: Awake and in bed and the alarm rings so you remain Awake in bed and turn it off
Present State | Alarm | Weekday | Next State | Turn off alarm
Asleep | Off | X | Asleep | No
Asleep | On | X | Awake in bed | Yes
Awake in bed | On | X | Awake in bed | Yes
Awake in bed | Off | Yes | Awake and up | No
Awake in bed | Off | No | Asleep | No
Awake and up | X | X | Awake and up | No
Notes: This state table covers all the cases.
  First row covers the situation you are asleep, the alarm is off and you remain asleep
  Last row covers the situation you are awake and up and you remain awake and up
  The third row covers the case you are awake and in bed and the alarm rings. You remain Awake in bed and turn it off.

## Slide 37: State diagram
Graphical representation of the state table
Each state = circle vertex
Each row of the state table = directed arc from:
  present state vertex to the next state vertex
Outputs are associated with the arcs
  Output of 1 = “turn off the alarm” is Yes
  Inputs which are don’t care and inactive outputs are not shown
Notes: Here is the state diagram for the alarm clock example.
It is a graphical representation of the state table
Each state is represented by a circle vertex
Each row of the state table is represented as a directed arc from present state vertex to the next state vertex
The outputs are associated with the arcs
  An output of 1 represents that “turn off the alarm” is Yes
  By convention , inputs which are don’t care and inactive outputs are not shown

## Slide 38: State machines
Mealy machine (used in text):
  Associates its outputs with the transitions
  Format of the label of each arc is Inputs/Outputs
  Self arcs must be shown (because the output values are shown on the arcs)
Notes: The Mealy machine used in this text associates its outputs with the transitions.
  In addition to the input values, each arc also shows the output values generated during the transition; the format of the label of each arc is Inputs/Outputs.
  Self arcs must be shown (because the output values are shown on the arcs)

## Slide 39: Designing from System Specifications
From a set of specifications, we want to develop
  State Table
  State Diagram
Example 2. Modulo 6 Counter specifications:
  Counts 000, 001, 010, 011, 100, 101
  One input U:
    1 = increment,
    0 = don't increment
  Three outputs (bits): V2, V1, V0
  Output bit C is 1 when transitioning from S5 to S0 (remains 1 until first transition)
  Machine has 6 states, representing six outputs: S0 ... S5
Notes: To Design from system specifications, first develop the state table then the state diagram.
Lets look at another example of a modulo 6 counter
It counts in binary from 0 up to 5
It has one input – if it is 1 then increment the number – if it is 0 do not increment
It has three outputs – one for each of the binary bits
Output bit C is 1 when going from 6 to 0
The machine has six states – one for each number

## Slide 40: State Table for modulo 6 counter
Notes: Here is the state table for each case.

## Slide 41: State Diagrams for Modulo 6 Counter
Mealy Machine
Notes: And here is the Mealy machine representation for it.
Note the carry bit is represented as the leftmost binary digit in the output.

## Slide 42: Finite State Machines
Any Circuit with Memory Is a Finite State Machine
  Even computers can be viewed as huge FSMs
Design of FSMs Involves
  Defining states
  Defining transitions between states
  Optimization / minimization
    Above Approach Is Practical for Small FSMs Only
Notes: Any Circuit with Memory Is a Finite State Machine
  Even computers can be viewed as huge FSMs
The design of FSMs involves
  First defining the states
  Next defining the transitions between states
  Finally, it is optimized & minimized
Note: This approach Is Practical for Small FSMs Only

## Slide 43: State Encoding
State Encoding Can Have a Big Influence on Optimality of the FSM Implementation
  No methods other than checking all possible encodings are known to produce optimal circuit
  Feasible for small circuits only
Notes: State Encoding Can Have a Big Influence on Optimality of the FSM Implementation
  There are no methods other than checking all possible encodings are known to produce optimal circuit
  Again, this is feasible for small circuits only.

## Slide 44: Types of State Encodings
Binary (Sequential) – States Encoded as Consecutive Binary Numbers (used in the text)
  Small number of used flip-flops
  Potentially complex transition functions leading to slow implementations
One-Hot – Only One Bit Is Active (used in many small real-world devices)
  Number of used flip-flops as big as number of states
  Simple and fast transition functions
Notes: Here are two types of state encodings:
In Binary or Sequential coding the States are encoded as Consecutive Binary Numbers. This is used in the text
  This uses a small number of used flip-flops, however it has potentially complex transition functions leading to slow implementations.
In One-Hot coding only one bit is active. This is used in many small real-world devices.
  The number of used flip-flops as big as the number of states, however it has simple and fast transition functions.

## Slide 45: Types of State Encodings (2)
State | Binary Code | One-Hot Code
S0 | 000 | 10000000
S1 | 001 | 01000000
S2 | 010 | 00100000
S3 | 011 | 00010000
S4 | 100 | 00001000
S5 | 101 | 00000100
S6 | 110 | 00000010
S7 | 111 | 00000001
Notes: Here is a comparison of the Binary coded state and the One-Hot coded state.
Review the Gumball Machine presentation for an example of two different encoding techniques and their effects.

## Slide 46: Inputs
FSMs change state based on clock edges
  I.e. Rising clock edge clocks all flip flops
This part can change only when clock “ticks”
Combinational Logic
For Next State
Comb. Logic For
Outputs
State
FlipFlops
Clock
Inputs
This part can change at any time
Synchronous Inputs: Change in synch with the clock. Obey setup and hold time.
Asynchronous Inputs: Change at any time. May violate setup and hold times.
Notes: Finite State Machines change state based on clock edges – For example flip flops change on the rising clock edge.
<click>
The section in pink can only change when the clock “ticks”
<click>
This is called synchronous Input. It changes in synch with the clock.
<click>
The section in blue can change any time.
<click>
It is called asynchronous Input. It changes irregardless of the clock.

## Slide 47: Asynchronous vs. Synchronous Inputs
Asynchronous
Synchronous
  Example: Elevator pushbuttons
  Arrive at any time
  Usually asserted for many clock cycles
  FSM logic must not make any assumptions about input timing
  Example: Data arriving on a serial line from a computer
  Arrive synchronized exactly to a clock
  One bit of data per clock cycle
  FSM can assume that data changes once per clock cycle
Notes: <click>
Elevator pushbuttons are examples of asynchronous input and the positions of the elevator are the various states.
They can arrive at any time and may be asserted for many cycles.
If the elevator is on 1 and buttons 3 &5 are pushed. The 5 must remain asserted after stopping at 3.
The logic can not make any assumptions about input timing.
All the floor requests will not be made at 1, someone may push 7 when moving from 3 to 5.
Synchronous inputs are much more controlled, for example data arriving on a serial line from a computer.
It must arrive synched to the clock and have one bit of data per clock cycle.
The FSM logic can assume that the data changes only once per clock cycle.
This is all on sequential circuits. Please review the presentation on Computer subsystems also before taking the quiz.
Also review the examples on the gum ball machine and the pattern matcher before doing the homework.